## Slide 1
Insulation Fixing Systems

## Slide 2
Head Pins with insulation
Insulated fasteners allow the fixing
in a single operation of aluminum
faced insulation such as lamella mats
or wired mats to the metal surfaces.
Head Pin Black with insulation
Insulated fasteners allow the fixing
in a single operation of black aluminum
faced insulation such as lamella mats
or wired mats to the metal surfaces.
D1 (mm) - 30
D2 (mm) - 2,2
L (mm) - 19÷250
D1 (mm) - 30
D2 (mm) - 2,7
L (mm) - 19÷250
D1 (mm) - 30
D2 (mm) - 2,2
L (mm) - 19÷250
D1 (mm) - 30
D2 (mm) - 2,7
L (mm) - 19÷250
D1 (mm) - 30
D2 (mm) - 2,2
L (mm) - 19÷250
D1 (mm) - 30
D2 (mm) - 2,7
L (mm) - 19÷250
Head Pins without insulation
Fasteners allow the fixing in
a single operation of non-aluminum
faced insulation such as lamella mats
or wired mats to the metal surfaces.
HVAC INSTALLATIONS

## Slide 3
Pin washer
Used to make sure that the insulation
material applied is held securely in place.
Alu Spots
D1 (mm) - 30
D2 (mm) - 2,2
L (mm) - 19÷250
D1 (mm) - 30
D2 (mm) - 2,7
L (mm) - 19÷250
D1 (mm) - 30
D2 (mm) - 2,2
L (mm) - 19÷250
D1 (mm) - 30
Pin size (mm) - 2,2 / 2,7 / 3
D1 (mm) - 30
D2 (mm) - 2,2
L (mm) - 19÷250
Spot diameter (mm) - 60
Spots on roll (pcs) - 750
Rolls per box (pcs) - 8
CD Pins without insulation
Used to fix thermal and acoustic insulation
to the air ducts or other steel constructions.
HVAC INSTALLATIONS
Aluminum Spots the optimal solution when it comes to cover pins heads. This is fast in installation, clean, a good looking, smooth, gapless and tight insulation surface. Delivered on the rolls.

## Slide 4
Lancing wire
Galvanized wire .
Alu Bands
D1 (mm) - 30
D2 (mm) - 2,2
L (mm) - 19÷250
D1 (mm) - 20
D2 (mm) - 8
L (mm) - 60 / 90 / 120 / 160 / 200
D1 (mm) - 30
D2 (mm) - 2,2
L (mm) - 19÷250
D (mm) - 0,6
Weight (g) - 100
Material - St 37
D1 (mm) - 30
D2 (mm) - 2,2
L (mm) - 19÷250
Spot diameter (mm) - 60
Spots on roll (pcs) - 750
Rolls per box (pcs) - 8
Fire Springs
A spiral screw made from galvanized steel wire coil.
It is used to connect edges of fire protection boards.
HVAC INSTALLATIONS
Pre-cut aluminum bands for pipe section and lamella mats installation.
Soon in the offer

## Slide 5
VBS Studs
Insulation studs VBS are used to fix
thermal and acoustic insulation to the aluminum
constructions (such as walls and decks).
Stud washer
Stud self-locking washers for securing
insulation on the studs.
Dome cups
Additional cover for the stud washers serves both
a protective and decorative purpose.
D1 (mm) - 30
D2 (mm) - 2,2
L (mm) - 19÷250
D (mm) - 3
L (mm) - 30÷1000
D1 (mm) - 30
D2 (mm) - 2,2
L (mm) - 19÷250
D (mm) - 38
Stud diameter (mm) – 3 / 4 / 5 / 6
D1 (mm) - 30
D2 (mm) - 2,2
L (mm) - 19÷250
D (mm) - 43
Stud diameter (mm) – 3 / 4 / 5 / 6
Colours – white, black, gray
MARINE CONSTRUCTION

## Slide 6
Self Adhesive Pins
Insulation pin with a self-stick base intended
to mount the insulation to steel duct surface.
Perforated Pins
An universal pin for insulation assembling.
Quick and uncomplicated fixing of insulation
on smooth, rough and uneven surfaces
(e.g. concrete, masonry, metal).
Pin washer
Washers for hold insulation on the pins.
D1 (mm) - 30
D2 (mm) - 2,2
L (mm) - 19÷250
D (mm) - 2,7
A (mm) - 50x50
L (mm) - 19÷240
D1 (mm) - 30
D2 (mm) - 2,2
L (mm) - 19÷250
D (mm) - 2,7
A (mm) - 50x50
L (mm) - 19÷240
D1 (mm) - 30
D2 (mm) - 2,2
L (mm) - 19÷250
D1 (mm) - 43
For stud clips
L (mm) - 19÷250
MARINE CONSTRUCTIONS

## Slide 7
ARC Stud
Insulation stud ARC are used when working
with tanks, boilers and other steel and stainless
steel constructions.
ISN Stud
Insulation stud ISN - for steel
or stainless steel construction.
Stud washer
Washers for hold insulation on the studs.
D1 (mm) - 30
D2 (mm) - 2,2
L (mm) - 19÷250
D (mm) - 3 / 4 / 5 / 6
L (mm) - 30÷3000
D1 (mm) - 30
D2 (mm) - 2,2
L (mm) - 19÷250
D (mm) - 2 / 3 / 4
L (mm) - 30÷245
D1 (mm) - 30
D2 (mm) - 2,2
L (mm) - 19÷250
D (mm) - 38
Stud diameter (mm) – 3 / 4 / 5 / 6
INDUSTRIAL CONSTRUCTIONS

## Slide 8
Quilted surface
For the products up to 50 kg/m3 use the pins with the length little bit smaller than nominal insulation thickness
(example: for insulation thickness 30mm use 28,5 mm pins) .
Right pin length
Flat surface
For all densities use the pins with the length little bit higher than nominal insulation thickness
(example: for insulation thickness 30mm use 33 mm pins).
Depending on the final effect you may use two different length of the pins.

## Slide 9
Fire Springs
Typical Fire Springs lengths: 30, 40, 50, 60, 80, 100, 120.
Fire Springs - description

## Slide 10
How to place on order
Information needed when ordering:
Pins – product name, with or without insulation, length, number of buckets/boxes (MOQ 1000pcs),
Studs – product name, diameter, length, material
Fire Springs - length, number of boxes (MOQ 250, 500pcs),

## Slide 11
Welding on protected surfaces
Protective coatings are the most widespread solution for protecting steel against corrosion. Anti-corrosion primer is generally applied immediately after steel is manufactured in order to prevent rusting during storage and transportation, and before further processing (cutting, welding, pinning, drilling, etc.).
The recommended anti-corrosion primers are often too thick (~50μm) for welding and need to be removed before welding or pinning. Removal is usually performed by grinding.
There is possible to find new primer products on the market which claim to provide good corrosion protection and to be weldable. These products often need to be applied in thin layers to be weldable (about 25 microns thick coating to enable an arc to strike through and reduce the chances of porosity due to their zinc content).Where primers are thin enough (~25μm) to allow welding, their anti-corrosion properties are limited that it does not reduce the corrosion. That is why they are not often used.